- Parts of terrain which are not visible, should not be rendered at all, because mesh can not mimic the terrain (probably because of LOD changing the terrain mesh), and terrain height can be seen. That means the only way to hide the terrain is to use custom shader. But how to hide water ? Create a plane, place it above water, and apply FoW texture onto it.

Following procedure with mesh covering the terrain doesn’t work :
- Generate mesh based on terrain – maybe it can be obtained from terrain ? (also include water)
- You must divide mesh into smaller parts (because of 65000 vertices limit)
- Place it above terrain (0.05 units above)
- Generate texture for a mesh (should be as large as possible up to the size of terrain)

- Create transparent circles on a texture for areas which are visible to player
- Disable renderers (and all rendering stuff) on objects which are not visible to player

1. method
- use render-to-texture to draw circles to texture ; this texure will be attached to FOW mesh ; but we can’t know if object is visible, we will have to copy texture from GPU – this can’t be done on dedicated server, because he may not have a GPU
2. method
- draw circles on CPU (maybe multithreaded), copy texture to GPU ; this way you will always know if object is visible, but it takes time to copy texture (if only you could copy it asynchronously)
3. method
- combinations of 1st and 2nd method ; only, you don’t need to copy texture to/from GPU

Solution : use first method for visuals, and for game logic see below.

why do we need visibility map ? - it’s too performance demanding – why cant we use 1st method ?
- building placement ;

Visibility map timings :
200x200 map, 300 units, 18 ms (15 ms filling circles, 3 ms resetting texture)
500x500 map, 100 units, 12 16 16 18
500x500 map, 200 units, 12 22 22 24
500x500 map, 300 units, 12 27 27 30
- maybe we can avoid resetting texture by filling circles in 2 textures (1st for LOS, 2nd for explored area), or by setting frame count when certain pixel was visited (or fill count) – but it has to be renderer using a shader (well, this is a visibility map, and won’t be rendered at all)

Multithreaded timings :
500x500 map, 700 objects, 65 ms per country

Lookup for visibility of an object :

- for 1. method :
If object is friendly, he is visible. If not, then object will get notified when he is scanned, and he can remember if he was scanned by local player country, in which case he is visible.
So, each object should have following :
- Dictionary<Country, int> - int => frame count when was scanned
- IsObjectVisibleByCountry (Country) – returns true if CurrentFrameCount – FrameCountWhenScanned > 0
- OnScannedByCountry (Country) – updates frame count for specified country
- it can also cache frame count when was scanned by country that is friendly to local player – allows really fast lookup for visibility by local player
As you can see, there is no need for removing anything from dictionary, so there is no need to iterate through dictionary at all => gives constant time.
Clients would also need to do scanning.

- for 2. method :
Just check pixel above object - it’s very fast, and doesn’t require scanning (but scanning must be done anyway :D). And also, we can make a lookup for every point on map, while with the 1st method, we can’t. Server would need to ‘draw’ circles for every object, and keep a visibility map for each nation separately, while the clients would need to ‘draw’ circles for countries friendly to local player.

FogOfWarObject.Update() timings :
- 160 objects, 0.4 ms – without checking friendly countries
- 700 objects, 3.5 ms

OLD:

For enemy objects : each friendly object should remember which enemy objects are visible to it. We are already scanning for all enemy objects. But when to disable renderers on enemy objects ? - Each enemy object should have a collection of (our) friendly objects which can see him. When the collection becomes empty, he disables himself. Friendly objects will notify them when they are no longer visible.

So, each object has a hashtable of objects which he can see, and a hastable of objects which can see him. When scanning for objects, we first check if they exist in a hastable, and if they don’t, we notify them that we can see them now. But how to notify them that they are no longer visible ? - if we don’t notify them for 2 frames, then he will know that he is not visible.

Time complexity : for areas – all objects will lighten up areas for their friendly countries, inside Update(), so complexity is O(1) ; scanning (already done)
Max memory : O(fo * eo + eo * fo)

When resetting texture transparency, remember what was painted last time, and then just reset those parts (if they are changed at all).